## Slide 1: Adhoc Networks
Brett Paris, Connor Rehbein, Austin Mease

## Slide 2: What isn’t an adhoc network
Google “how to set up adhoc network”
  Most of these results are actually wireless hotspots

## Slide 3: What is an adhoc network?
Collection of wireless mobile nodes dynamically forming a temporary network without the use of an existing infrastructure or centralized administration

## Slide 4: How to set up on linux
read -p "network card: " card
read -p "IP address: " address
sudo service network-manager stop
sudo ifconfig $card down
sudo iwconfig $card mode Ad-hoc
sudo iwconfig $card essid MyWifi
sudo ifconfig $card up
sudo ifconfig $card $address netmask 255.255.255.0

## Slide 5: Take down
read -p "network card: " card
sudo ifconfig $card down
sudo iwconfig $card mode Managed
sudo ifconfig $card up
sudo service network-manager start

## Slide 6: Testing site: James Madison park

## Slide 7: 1Hop
Chart: TCP Bandwidth v. Distance
| 9.167 | 18.334 | 27.501 | 36.668 | 45.835 | 55.002 | 64.169 | 73.336 | 82.503 | 91.67 | 100.837 | 110.004 | 119.171 | 128.338 | 137.505 | 146.672 | 155.839 | 165.006 | 174.173 | 183.34 | 192.507 | 201.674 | 210.841 | 220.008 | 229.175
 | 1.8 | 1.3 | 1.51 | 0.65 | 0.832 | 1.41 | 0.846 | 0.946 | 0.555 | 0.469 | 0.66 | 0.733 | 0.751 | 0.497 | 0.496 | 0.185 | 0.09 | 0.227 | 0.195 | 0.0994 | 0.0938 | 0.0853 | 0.118 | 0.0478
Chart: UDP Bandwidth v. Distance
| 9.167 | 18.334 | 27.501 | 36.668 | 45.835 | 55.002 | 64.169 | 73.336 | 82.503 | 91.67 | 100.837 | 110.004 | 119.171 | 128.338 | 137.505 | 146.672 | 137.505 | 146.672 | 155.839 | 165.006 | 174.173 | 183.34 | 192.507 | 201.674 | 210.841 | 220.008 | 229.175
 | 0.659 | 0.79 | 0.794 | 0.573 | 0.933 | 0.722 | 0.69 | 1.04 | 0.429 | 0.492 | 0.755 | 0.331 | 0.932 | 1.03 | 0.309 | 0.517 | 0.398 | 0.401 | 0.2 | 0.269 | 0.239 | 0.409 | 0.506 | 0.303 | 0.208 | 0.217 | 0.035

## Slide 8: 2Hop

## Slide 9: RELEVANCE TODAY: internet without isp